## Slide 1: System Data Acquisition & Management at PHELIX
Jonas B. Ohland, Udo Eisenbarth, Stefan Götte

## Slide 2: Agenda
PHELIX in a nutshell
The PHELIX Control System (PCS)
The PHELIX Shot DataBase (PSDB)
  Motivation/Design considerations
  Snapshot data
  Time series data
  Data access

## Slide 3: PHELIX in a nutshell
Two front-ends: - short pulse “fs” - long pulse “ns” - coming soon: incoherent ns
Nova-type Nd:Glass main amplifiers => 1 shot/90 min, => 6 shots/day
Three experimental areas: - Petawatt TA - Z6 (with UNILAC) - HHT (with SIS18)
User facility

## Slide 4: PCS Architecture
OS: Windows
  Cross platform compatible
LabVIEW 2019
  no higher version due to FireWire
  no lower due to many reasons
Distributed on 38 nodes:
  34 PCS
  2 developer
  2 hardware test nodes
one executable
about 146 PHELIX classes
  36 Base classes
  about 500 instances
about 10000 process variables
PCS nodes in the PHELIX laser hall (selection)

## Slide 5: PCS Interfaces (selection)
Shot Sequencer (state machine)
Beamline GUI
Motion control
Security monitoring/control
Data acquisiton/visualization/logging

## Slide 6: PHELIX shot database (PSDB)
Primary motivation: tool for operating crew
  Search and compare shots
  Generate statistics/identify trends
  Prepare similar shots
Requirements:
  Reliable (working for 12 years)
  Future safe (e.g. new data types, devices …)
  Group shots by experiments
  Easy access from everywhere
  As little maintenance as possible
Current PSDB web interface

## Slide 7: PSDB design considerations
Workflow
Snapshot structure
Data redundancy
Example: camera data
Data | Changes? | Type & size
Image | each shot | Image (~MByte)
Exposure | sometimes | Numeric (8 byte)
Serial # | rarely | Numeric (8 byte)
For each shot ALL data is written:
  information redundancy
  no versioning necessary
► Strongly reduced maint. effort
Shot
Id (Shot #)
Timestamp
Comment
Experiment
Shot type
Camera 1
Powermeter 5
Camera 2
Shutter 4
Image:
Exposure: 20 µs
Image:
Exposure: 15 µs
Energy: 123 J
Position: open
Create experiment entry
via web interface
once at beginning of experiment
Shot procedure
Select experiment
Select shot type (test/experiment)
Press shot button
Add/modify shot comment
via web interface
Attach additional shot files
via web interface

## Slide 8: PSDB ↔ PCS com. on Shot delivery
User
PCS
PSDB
Data controller
Device
Device
Device
Sequencer
PCS Start Up
Shot Delivery
Name
Device
ID
possible
Experi-
ments,
Shottypes
Preparation
Sequencer
Data controller
Sequencer
Experiment,
Shottype
possible
Experiments,
Shottypes
Experiment,
Shottype
Data controller
Shot
Start
Standby
Shot
ID
Write with
Shot ID
Data
Device
Device
Device
Device
Device
Device
Status

## Slide 9: Logical Data structure
Shot
Shot #
Timestamp
Experiment #
Shot type
Shot comment
Shot type
Test shot
Experiment shot
Snapshot
Experiment
Internal
P010
P018
P155
…
Best shot ever, blah…
2010-25-1 15:00
Automatically assigned
Device Data
Data types
Numeric, String,
Image, Spectrum,
…
Devices
PA_Input_NF_Cam
MAS_Filt1_BB
MAS_Spectrometer
…
Shot # | Device # | Parameter | Data type | Data
4711 | 1 | Shutter | Numeric | 412
4711 | 1 | Picture | Image | 
4711 | 2 | Filt_in | Numeric | 1
4712 | 1 | Shutter | Numeric | 515
4712 | 3 | Spectrum | Spectrum | 
… | … | … | … | …

## Slide 10: Database Structure
Device Definition
Shot Definition
Granular Data Entries
Device Data List
Recent development:
Time series
Instance ID Number
Timestamp Date
Value Number
Range Min. Number
Range Max. Number

## Slide 11: Time Series Measurements
Web interface view of a humidity time series
Periodic logging of numeric data chunks
Intended for sparse monitoring
Not optimized for high-throughput
  Every data point is a DB entry
  => Easy access & low maintenance

## Slide 12: Data Access
PSDB
Webserver
https://psdb.gsi.de
Application written in Ruby on Rails
Web browser
View & Export data to file
Open API
Direct, programmatical data access
Current PSDB web interface
Online API documentation

## Slide 13: Conclusion
PCS:
  Distributed system
  Easy & robust shot data acquisition
  Asynchronous logging to PSDB
  No real-time capability
PSDB:
  Intended for operator use
  Robust and flexible layout
  Designed for low repetition rates (low throughput)
  Optimized for low maintenance
  Data programmatically accessible via API

## Slide 14
Jonas B. Ohland (random presenter):
phone: +49 6159 71 3381
email: j.b.ohland@gsi.de
Udo Eisenbarth (PSDB developer):
phone: + 49 6159 71 1301
email: u.eisenbarth@gsi.de
Stefan Götte (PCS developer):
phone: +49 6159 71 1445
email: s.goette@gsi.de