## Slide 1
Sonde Floating Detection
Fluid Level Detection
Core Break Detection
Electronics in the Borehole
2m/s
1m/s
0m/s
1m/s
Pay In
Pay Out
Surface Operations
Fluid Transition
2m/s
Cutting Zone
Air
Fluid
Pay in speed may be limited by power available.
System sees maximum power usage during pay in through fluid. The peak is at top of fluid column where cable drum wrap radius is largest. This is also the point of maximum winch torque.
Maximum cable tension occurs at core break.
This is also the moment of maximum force on the tower.
Cable Speed
Pay out speed is limited by terminal velocity of sonde in fluid.
If cable speed exceeds the sonde speed, loose cable will eventually create a knot in the borehole!
Time
Cable Tension
Window
Threshold
Hard Break
Soft Break
● Detect Core Break
● No Core Break
To detect core break, the system captures the peak tension following a rapid decrease in cable tension from the peak. This avoids detecting the sonde weight as a “core break” tension if there is a soft break, common in firn. Core break detection is enabled once per core, to avoid detecting “core breaks” due to cable tension transients associated with ringing after a hard break and/or fluid transition under tension.
In the figure below, core break is detected when the cable tension decreases below (peak-threshold) within (window) milliseconds.
Ice
Time
Force
Transient from winch acceleration
Fluid impact
Buoyant force accumulates
WOB
WOBBaseline
∫(WOB-WOBBaseline)dt
Threshold
Automated fluid level detection occurs once per drill run, and is based on the integral of the difference between the WOB and the WOBBaseline, which has been passed through a low-pass filter (LPF); i.e. ∫(HPF(WOB))dt. When this signal exceeds a threshold, the fluid level is updated based on the payout. The integral is zeroed when the winch is accelerating to avoid triggering on WOB transients associated with changes in winch velocity.
Other methods for fluid detection may offer more precision, but this is an economical solution to a common problem which may be implemented without modifying existing hardware.
This material is based upon work supported by the U.S. National Science Foundation under Cooperative Agreement No. 1836328 and Continuing Grant 2318480
NSF Ice Drilling Program University of Wisconsin-Madison1
Motion Profile in the Borehole
Umberto Stefanini1, Jay Johnson1
The sonde floats when the upwards force on the sonde (i.e. weight on bit , WOB) is greater than or equal to the nominal weight of the sonde. WOB is calculated from the cable tension as follows:
wob = gravity(latitude) * (sonde_kg + cable_kg_per_m * payout_m – fluid_density_kg_per_cc * est_submerged_vol_cc) – cable_tension_N;
The large number of inputs means that this function is susceptible to errors, especially ones that accumulate with payout (for example, due to the error in cable_kg_per_m ). Errors may also be incurred due to the elasticity of the cable, which is paid in or out under varying tension.
Additionally, the cable tension can be affected by forces applied directly to the cable, such as drag from the fluid or borehole wall. This affects the calculated WOB and so also contributes to errors in sonde floating detection.
Errors in calculated WOB contribute to an unreliable sonde floating detection. An obvious solution is to design sonde electronics that measure WOB directly at the sonde, but this is an expensive solution for existing equipment.
Because errors in the WOB seem to be a function of payout, they accumulate slowly. When the sonde floats, the calculated WOB becomes unresponsive to small changes in cable velocity, so automatically varying cable velocity when floating is a risk may offer a (slightly annoying) solution.
!