## Slide 1: High-Altitude Thermal Drilling
9th International workshop on ice Drilling Technology
9/17/2025
Elliot Moravec, Krissy Slawny, Elizabeth Morton, James Koehler

## Slide 2: Agenda
Thermal drill specifications
Quelccaya Ice Cap coring project (Peru)
Mt. Waddington ice coring project (Canada)
Sediment Challenges
Opportunity for discussion
Photo Credit: Mariusz Potocki

## Slide 3: Thermal Drill Specifications
  1800w heat ring melts 86mm (3.4”) core
  Normally paired with IDP 4-Inch winch and tower.
  Intended for use in isothermal glaciers (ice warmer than -10C)
  Requires pooling melt water in borehole
  Collects ~2m core/per run
  300m water shedding cable implemented in 2019

## Slide 4: Investigation of High Andean Snow and Ice Chemistry to Improve Paleoclimatic Reconstruction and Enhance Climate Prediction - 2022
Project PI
Paul Mayewski (Climate Change Institute - University of Maine)
Location
Quelccaya Ice Cap in Peru
Drilling Objectives
Thermal drill 130m ice core to bedrock from summit of ice cap (5700m elevation)
Field test new debris vacuum and ethanol deployment systems
Photo Credit: Elliot Moravec

## Slide 5: Drill Disassembled for Transport to Summit
Project relied on porters and horses for cargo transport
Max cargo piece weight of 90lbs
Drill, winch, generator (6.5kW) disassembled for transport
All ice cores transported by porters off summit
Photo Credit: Elliot Moravec

## Slide 6: 128.3 m Core Drilled Over 5 Days
  Excellent core quality (almost no breaks)
  Warm daytime conditions required night operations while in firn
    1.5m/hr core production rate in firn
    50% heat ring power max in firn
  3m/hr core production rate in ice when pooling water present
  53.8hrs drilling required to reach a depth of 128.3m
Photo Credit: Mariusz Potocki

## Slide 7: Ethanol Added Daily to Borehole to Prevent Refreezing
Ethanol “shots” contained in layflat tubing.
Shots deployed to bottom of borehole in drill sonde
Pointed plunger punctures layflat and forces ethanol into borehole
Ethanol deployed once per night, ~1gal per shot
Limited issues with sonde sticking in borehole while tripping
Section View of Ethanol Deployment System

## Slide 8: Collaborative Research: P2C2-- Ice Core and Firn Aquifer Studies - 2023
Project PIs
Peter Neff, Eric Steig, Knut Christianson
Location
Mt. Waddington, British Colombia
Drilling Objectives
To collect a ~240 m ice core to bedrock at Mt. Waddington for development of the southern-most annually-resolved ice core paleoclimate record in North America.
Photo Credit: Elizabeth Morton

## Slide 9: 247 m ice core drilled over 15 days
  Borehole #1 cored to 208 m depth
    Rock at-depth prevented further progress
  Deviated from borehole #1 between 174-180 m over two coring runs.
  Replicate coring progressed to 219 m depth.
    Accumulated sediment prevented further progress
  Additional deviation not successful
    Not enough inclination
Photo Credit: Elizabeth Morton

## Slide 10: Challenges – Mt. Waddington
  Debris layers caused slow penetration and core necking
    Small diameter core caused recovery issues
  Sediment and rocks accumulated in melted annulus stopping drill penetration
  Future Work – Design conical melter head for debris recovery.
    Melt debris into center of borehole
    Core around debris with traditional coring setup.
Photo Credit: Elizabeth Morton

## Slide 11: Opportunity for Questions
Potential Discussion Topics
Pressure rated electrical connectors
Solutions for downhole rock and sediment accumulation
Thank you for your time!
This material is based upon work supported by the U.S. National Science Foundation under Cooperative Agreement No. 1836328 and Continuing Grant 2318480.