## Slide 1
Presented by:
Kevin Nikolaus
The MiniLogger System
Notes: ##-AccessibilityAssistant: Skip layout check-##

## Slide 2: Overview
Motivation
Focus: Standalone, low-weight borehole logging tool
The ISD4000, a sensor borrowed from the oceanographic world, provides high quality temperature, pressure, and orientation measurements. We designed a simple self-powered logging device to record this data, no special winch or cable required.
ISD4000
Impact Subsea
Depth, Temperature
& Orientation Sensor

## Slide 3: Overview of the Electrical Design
Openlog Artemis
Features
On board data logging
Robust single cable connection between sensor and logger
Power System
Shorting plug in wet cable automatically starts system upon connection
Low power electronics allow for long endurance
Misc.
Pressure relief value to seal under vacuum to ensure good seal prior to use (using internal PHT sensor)
3
3.6 V C Cell Battery
3.6 V C Cell Battery
3.6 V C Cell Battery
OpenLog Artemis
Power
Linear
Regulator
3.6 V C Cell Battery
3.3V
14.4V
Comms
RS232 to TTL
Converter
Pressure
Relief Port
8 Pin Subconn
PHT Qwicc Sénsor
Bluetooth
Data Transfer