## Slide 1
A new dynamometer for testing ice core drill motors and gears.
Matthias Hüther1, Frank Wilhelms12
1Alfred Wegener Institute, Helmholtz Centre for Polar and Marine Research, Bremerhaven, Germany 2Georg August University of Göttingen, Department of Isotope Geology, Göttingen, Germany

## Slide 2: Motivation
Failed to provide working motor with sufficient torque for BEIO drilling
Failure not detected early:
  Ambitious goals and
  Missing full system testing capabilities

## Slide 3: Existing Test Stands
Testing Motor on drill cable:
  Without mechanical load
  Peak torque, blocking
  Break module
Testing in the Field
  Break module was build for testing in EDML Borehole

## Slide 4: Makeshift Test stands

## Slide 5: Envisioned Use cases
Evaluation of current drill motor limitations
Testing current motor with new gear
Potential new motor designs
Comparison testing between ice core drill motors

## Slide 6: Design Goals
Dynamometer for workshop at AWI
Simulating of full coring run duration
Break Torque ~ 0 – 100 Nm
RPM ~ 0 – 200 1/min
Measuring torque and RPM
If possible simulate different torque path:
    Internal: Pump / Chip transport
    External: Drill head / Ice cutting

## Slide 7: Mechanical Setup
Off-the-shelf disk break
Existing incremental encoder
Cheap load cells
Reuse drill parts
Aluminum extrusion frame
Manual hydraulic breaks
Optional Break control

## Slide 8: Internal / External Break
External
Internal
Single Disk
Two Breaks
Two Load Cells

## Slide 9: Electronic
Single PCB
Support for two load-cells
Encoder interface
Standalone displays
USB Serial for “fast” live Data
USB DP as power supply
Two stepper motor interfaces
Buttons and E-stop

## Slide 10: Current State
Mechanics mostly assembled
PCB v1.0 in production
Firmware feasibility studied
Next step:
Testing electronics
Firmware implementation of sensors

## Slide 11: Missing Capabilities
Motor / gear not submerged
Limited temperature and pressure simulation
Unknown dynamic behavior / drill characteristics

## Slide 12: Questions
Thanks for your attention.
Any questions?

## Slide 13: Abstract
Specialised test equipment is frequently required during the design and verification phases of a project. However, this equipment is often expensive, not always readily available at the time, or just time-consuming to use. This can result in reliance on systems that have not been adequately tested prior to field campaigns. This may lead to system failures or substandard designs.
This newly designed dynamometer is intended for use in testing motors and gears of ice core drills. The aim is to resolve the issue of a missing test facility by using off-the-shelf components in its construction, with a relatively small and user-friendly form factor.
This presentation will introduce the design concept and its intended use cases.