## Slide 1: Collected topics
1.) How deep can we safely dry-drill?
2.) How do we find/train/retain on non-permanent staff and in times of inconsistent funding/deployments?
3.) Unknown variables in regards to rock drilling? No clear data
4.) How do we host sharing? Side hosting files icedrill.org
5.) Semi regular meetings?
6.) Next Conference?
7.) More formal frame (e.g. working group with IGS, ...)?
8.) Failures you normally do not talk about.

## Slide 2: How deep can we safely dry-drill?
Rapid access hole, depth of 5-700 m dry
1 cutter to have smaller diameter when stopped
461 max.
Program how long you can spend at any depth (Rob), warmer site problematic.
Left drilling over night, reached limit how deep you can go.
Low power winch
What is the closure rate.
Step cutters only one having the full diameter

## Slide 3: Unknown variables in regards to rock drilling? No clear data
Core breaks, Elliot might have compiled information
Pdc tooth cutters
Not enough weight on bit
Not enough flushing
Not enough rotation speed
Diamond impregnated bits, change tip geometry -> more pressure
You have to crush rock, not shear it, you need high bit pressure
Pdc bits cut ICE quite nicely, diamond impregnated bits glaze quite easily

## Slide 4: Failures you normally do not talk about.
Mount multi start (trapezodial) threads with torque, settle with ice very efficient. Had to heat to break apart.
Glycol attacked slip ring
Epoxy raisin pipe -> talk from Darcy tomorrow
Eclipse drill at summit, raised tower vertical, dropped meter to a halfmeter, huge bang
Community paper on failures -> coordinated by Keith for hot water drilling
Big raid, a little stuck on the way up, not clear why it happened (hole not straight?)
Checklist what you should check, pull test, hook on the drill
Warning on software when going into liquid, load drop due to too high speed
Training software for new drillers, AI technology, combined with software
Objective way to describe good core quality -> pieces per run, IDP core quality score
Time pressure a problem –> list should be empty
All incidents go to a list, error culture
What went wrong what people have tried
Failure (Arasystem): rushed, shifts divided, frozen drill, effort to save fuel, disconnected drill head, almost froze entire drill, people pushing to go upper management, pushed back first time driller
Not just equipment be damaged, also people can get injured, slowing down enough time

## Slide 5: How do we find/train/retain on non-permanent staff and in times of inconsistent funding/deployments?
Payment, worldwide competition, big database and connect people, database for suppliers, traceparts
Specialised contractors very expensive
Specialised database
Attitude to keep people and hire them back
Drilling for scientists
Fight stubbornness of administration
Liaising with private companies who have people that want to go on expedition and can have them going
Recognition on highest level that network has to be done, sending out people to interact.