## Slide 1: Pathfinder Instrumentation for SPRING TauSoL Imaging SpectroPolarimeter Hemanth Pruthvi ● Hans-Peter Doerr ● Michael Sigwarth ● Markus Roth
Spanish‐German WE-Heraeus-Seminar
Bad-Honnef, Germany
03.07.2025
Optical Instrumentation Group
Thüringer Landessternwarte (TLS)
Tautenburg, Germany

## Slide 2: SPRING
Solar Physics Research Integrated Network Group
For synoptic observations of the Sun

## Slide 3: Synoptic Observations
Full disk recordings
Spanning decades
Ground or space-based
Ideally, uninterrupted
Cadence of a minute or less

## Slide 4
ESA
Helioseismology
NASA
Solar Activity
NASA
Long-term Variability
ESA
Space Weather
SPRING Motivation

## Slide 5: SPRING and GONG
Operational since 1995
Solar interior
Solar activity forecast
End of Life (SDO too!)
What’s next?

## Slide 6: SPRING Science Requirements
Instruments
  Filtergraph(s)
  Imaging SpectroPolarimeter(s)
  Scanning SpectroPolarimeter(s)
  Integrated Spectrometer(s)
Region of interest
Full disk; arcsecond resolution
Observables
Intensity, velocity, magnetic field …
Spectral lines
Photosphere to upper chromosphere
Cadence
Few seconds to few minutes

## Slide 7: SPRING Concept Studies

## Slide 8: TauSoL Towards SPRING Node-0
Light-feed system Depressed polar siderostat
Optical benches For experimentation
40 ft container
Tautenburg Solar Laboratory

## Slide 9
TauSoL First Light & Inauguration

## Slide 10: Instrumentation Imaging SpectroPolarimetry
Intensity (Stokes-I)
Linear Polarization (Stokes-U/I)
Linear Polarization (Stokes-Q/I)
Circular Polarization (Stokes-V/I)
SO/PHI

## Slide 11: Instrumentation Specifications
Telescope size | 100 mm | Maximum 180 mm
Wavelength range | 510 – 710 nm | Maximum 510 – 860 nm
Spectral Line | Fe I 630.25 nm | With Telluric blend for reference
Tunable Filter System | Fabry-Pérot Interferometer Ultra-narrowband filter Broadband filter | Piezo-tunable; 0.96 mm air-gap ICOS ET150 – 150 mm aperture Order sorting; 0.1 nm bandwidth Blocking; 1 nm bandwidth
Polarimeter System | High-speed liquid crystal variable retarders Polarizing beam splitter | Polarimetric modulation Dual-beam analyzer
Image stabilization | Piezo tip-tilt corrector | With correlation tracking
Sensor | CMOS cameras | 20 MP Gpixel GSPRINT4521
Telescope size | 100 mm | Maximum 180 mm
Wavelength range | 510 – 710 nm | Maximum 510 – 860 nm
Spectral Line | Fe I 630.25 nm | With Telluric blend for reference
Tunable Filter System | Fabry-Pérot Interferometer Ultra-narrowband filter Broadband filter | 
Polarimeter System | High-speed liquid crystal variable retarders Polarizing beam splitter | Polarimetric modulation Dual-beam analyzer
Image stabilization | Piezo tip-tilt corrector | With correlation tracking
Sensor | CMOS cameras | 20 MP Gpixel GSPRINT4521

## Slide 12: Instrumentation Design
Collimated
Configuration
Telecentric
Configuration

## Slide 13
Early stages of Assembly
Prepared for data acquisition
Exploring alternative technologies
Lithium Niobate FPI
Instrumentation Status

## Slide 14: SPRING Path Forward
Research and Development
  Infrastructure design
  Next-gen instrumentation (viz., high-cadence multi-line spectropolarimeters)
International SPRING Consortium
  GONG site partners
  Solar science community
  Space weather community

## Slide 15: In Short …
Synoptic solar observations have become indispensable Furthering the fundamental knowledge Preserving the technological modernity
SPRING is the Next-Gen Several facilities approaching EOL Interdisciplinary solar science consortium
TauSoL is a Pathfinder Already operational, instrumentation in-development Visitors are welcome!

## Slide 16
Thank you and questions?

## Slide 17: Calibration Spectral line
Fe I 630.25 nm The “technical line”
High sensitivity to magnetic field Landé-g = 2.5
Telluric line blend For wavelength calibration

## Slide 18: Polarimeter
Dual-beam polarimetry
Two liquid crystal variable retarders as modulator system
Polarizing beam splitter as analyzer

## Slide 19
Outlook

## Slide 20: Spectrometry
Tunable filtergraph 2-D spectrograph
A single Fabry-Pérot interferometer (FPI)
Ultra narrow passband interference filter

## Slide 21: How? Solar Observations
BASS2000

## Slide 22: ngGONG – SPRING update meeting Feb. 21, 2025
Outline:
TauSoL 1st light and inauguration / next steps
Start of LiNbO3 wafer development
Outcome of Heliophysics Decadal survey – next steps
Planning's at TLS for SPRING
Formation of a SPRING community: gathering interest and partners
Notes: Will give a brief overview to the main instrumentation projects and tasks of the new group
Which is a new solar telescope and lab on site here,
Introduce plans for upgrading the 2m Alfred Jensch telescope
and very short motivate “networking activities”
There are also posters to motivate the scientific background of these instrumentation projects and on SolarLab itself.

## Slide 23: TauSoL
Tautenburg
Solar
Laboratory
At TLS Tautenburg

## Slide 24: TauSol first light and inauguration Sept-Oct 2024
1st light 18. Sept. 2024
Notes: Container based concept was not only chosen because of cost and time.
Very likely the next synoptic network instrument will also need to be container based.
So the container based design is part of the “prove of concept”