## Slide 1: Tango Introduction
pyAML Community Meeting 2025.09.04 B. Bertrand (MAX IV)

## Slide 2: What is Tango 1/2
“Tango Controls is a free open-source device-oriented controls toolkit for controlling any kind of hardware or software and building SCADA (supervisory control and data acquisition) systems. Tango Controls is operating system independent and supports C++, Java and Python for all the components”

## Slide 3: What is Tango 2/2
Started in 1999 @ESRF Synchrotron in Grenoble, France
Used by Synchrotrons, lasers, telescopes…
Rich ecosystem (Archiving, GUI, Tools)
Based on CORBA and ZeroMQ
Built around the concept of devices and device classes

## Slide 4: Tango Key Concepts

## Slide 5: Device
A device is an object providing access to commands, attributes and properties
A device can represent:
A piece of equipment
Multiple pieces of equipment
A set of software functions
A group of devices representing a subsystem
Notes: A device is a key concept

## Slide 6: Device name
Every device has a 3 fields name, following a hierarchical notation: domain/family/member
sys/database/2
sys/tg_test/1
i-c080008cab02/vac/ipcua-04 (Ion Pump)

## Slide 7: Device Commands
Operation to invoke on a device: SwitchOn, SwitchOff
Every device has at least 3 commands:
  Init
  State
  Status

## Slide 8: Device Attributes
An attribute represents a typed variable with a value
Data format: Scalar (0D), Spectrum (1D) or Image (2D)
Data type (boolean, short, ulong64…)
Read and/or Write
Metadata: quality, timestamp
State and Status

## Slide 9: Device Properties
Configuration parameter stored in the Tango Database
Represented as key-value pairs

## Slide 10: Device Server
A Device Server is the process that will create devices of a Device Class (an abstraction of a device’s interface)
{DeviceServerName}/{instanceName}

## Slide 11: Tango Database
Each Tango Controls system has a centralised Tango Database
  Maintains a catalog of the Tango device servers and devices configured to run in the sytem
  Stores configuration data (properties) used at initialization of a device
  Acts as name server
  Stores dynamic settings (memorized attributes)
Databaseds device server
PyDatabaseds device server
Not production ready - Testing only

## Slide 12: TANGO_HOST
Variable that specifies on which host and port the Databaseds is running: localhost:10000
Can be set using:
  environment variable
  /etc/tangorc on unix-like OS
  ${TANGO_ROOT}/tangorc on Windows
  ~/.tangorc on unix-like OS

## Slide 13: Tango Controls System Communication
Databaseds device server
TANGO_HOST
PowerSupply device server
test/power_supply/1
Server
Client
DeviceProxy(’test/power_supply/1’)
1. Device Server tells Databaseds about its connection details (IP, hostname, port)
2. Lookup device & connection string
3. Connect to Device Server

## Slide 14: PyTango

## Slide 15: PyTango
Module that exposes to Python the Tango C++ API
Write Tango Device Server
Access the Tango Database
Write Tango client (script, CLI, GUI)

## Slide 16: PyTango Device Server

## Slide 17: PyTango Client 1/3

## Slide 18: PyTango Client 2/3

## Slide 19: PyTango Client 3/3

## Slide 20: Useful Links
https://www.tango-controls.org
https://tango-controls.readthedocs.io
https://pytango.readthedocs.io
https://tango-controls.readthedocs.io/en/latest/Tutorials/getting-started/00--tutorial.html