## Slide 1: Bunch by Bunch BPM measure at SOLEIL
Nicolas HUBERT on behalf of Romain BROUCQUART
DEELS 2022

## Slide 2: Origin of this measure
Using a fast camera, we captured the turn-by-turn emittance during injection
The beam size was increasing → not physical
"painting" of the spot of the camera by intra-turn position evolution ?
Quick answer → yes. But let's focus on the diagnostic…
Introduction

## Slide 3: Measure Setup
Libera Digit500 connected to BPM Pickups
Sampling rate on the main RF, phase manually adjusted
Capture on request or on injection.
Introduction

## Slide 4: Bunch response
Single bunch, 16mA.
Manually scan the sampling phase.
Trigger 3Hz, synchronous to revolution frequency.
Plot the average signal value of the bunch sample over multiple turns.
(!) X-Axis is distorted by the manual scan.
Give an idea of cable phasing and bunch response.
Position the sampling phase at the center point of maximum.
Introduction

## Slide 5: Phase adjustment
Sampling phase of each ADC can be programmed independently.
We use that feature to perform gross and fine scan.
Need to be quick to avoid effect of current decay (< 10s).
Fast full scan
Precise local scan
Introduction

## Slide 6: Filling Pattern
Wrap data with a periodicity of 416 (number of bunches in SOLEIL).
Observe the sum signal.
Align Trigger and bunch index.
Skip low filled bunches for position processing (high SNR)
Introduction

## Slide 7: Problem : Betatron Frequency
Observation on bunch by bunch sum / position
Signal is decimated by 416
Fsampling = frev (847 kHz)
Spurious at 123 kHz on X position.
Sometimes occurs
Probably betatron frequency
Introduction

## Slide 8: Problem : Betatron Frequency
Frev
2*Frev
4*Frev
726 kHz
Introduction
Observation on raw signal
Fsampling = frf (352 MHz)
726 kHz = frev – 123 kHz

## Slide 9: Injection capture
The next captures are performed while kicking the beam for injection.
With or without charges injected.
Data are aligned so that the charge enter the storage ring on turn 0.
Data visualization

## Slide 10: How to visualize the data ?
Data visualization

## Slide 11: How to visualize the data ?
Animation plot
Each frame is a turn
X-axis is the bunch number (quarter profile)
Data visualization

## Slide 12: How to visualize the data ?
Data visualization

## Slide 13: How to visualize the data ?
Waterfall plot
Each line is the position evolution of a bunch (one over two taken).
Each line is offseted by 100 µm
Data visualization

## Slide 14: How to visualize the data ?
Colored plot
Quasi direct plot : each point is a sample
Color each point by its quarter
Data visualization

## Slide 15: Link to turn by turn from eBPM
Colored line : turn by turn with mask over one quarter.
Black line : total turn by turn data.
Data visualization

## Slide 16: Evolution of sum signal
Evolution of sum signal → effect of bunch phase (stored + injected)
Background removal by estimating common mode on the 3 quarters and removing it on the injected one.
Common mode oscillation = 3920 Hz (Synchrotron Frequency)
Injected quarter oscillation = 8466 Hz (?)
Sum signal

## Slide 17: Evolution of sum signal
Mean and std of sum signal, bunch by bunch, over the whole capture
Mean
"Filling pattern"
Std
Proportional to charge injected to the bunch
Sometimes seems not aligned with stored beam → ?
Shape of injection → ?
Sum signal

## Slide 18: Position evolution, w/wo charge
For the injected buckets, position picked-up is the barycenter of the stored bunch and the injected charge
500 mA Stored
1,5 mA Injected
For this plot : averaging by grouping bunch 13 by 13.
Charge injection

## Slide 19: Consecutive injections
Only one quarter filled (pink)
Consecutive injections in the opposite quarter
Each measure is a mix of the stored (increasing) charge and the injected charge.
For this plot : averaging bunches 8 by 8
Charge injection

## Slide 20: Focus on injected electrons
Second injection in a quarter : the position is halfway between stored and injected charge.
Data aligned so that the injected quarter is always at the same x-axis phase.
6 turns periodic oscillations around the main trajectory, decreased after 70 turns
Charge injection

## Slide 21: Focus on injected electrons
Periodic damping of oscillation (250 turns) → phase oscillation of injected bunch
Charge injection

## Slide 22: Application idea
Let it run on several injection during operation
Automatically compute (and archive) some metrics
Link what is observed with the injection efficiency ?

## Slide 23: (TODO) Jitter sensitivity
Lab measure
Source channels and REF with identical source
Identify jitter with amplitude noise
On beam measure (idea)
Shift the phase so the jitter effect predominant over Q
From Instrumentation Technologies
Jitter : 1,4 ps rms
Introduction

## Slide 24: Focus on injected electrons
Offset of injected charge ?
One injected without the same phase (after a few hundred of turns)
Charge injection